Aastra / Asterisk - Quick Reference Guide

Phone model 6739i (39i)

Table of Contents

Standard Telephone Information

Button Descriptions	2
Making Calls	3
Transfer	3
Conference	3

Ring Tone	4
Contrast	4
Volume	4
Headset	4

Bluetooth	4

Optional Functions

Call Forward	5
Call List	5
Directory	5

Do Not Disturb (DND)	6
Follow Me	6

Keys	6

Logout	6

Meet Me Conference Bridge	7
Parking	7

Presence	7
Voicemail	8

Button Descriptions

Note: Throughout this manual the permanent keys listed above are referred to in GREEN print and the softkeys on the screen are referred to in BLUE print.

Making Calls

There are two methods to begin a call from the idle state of the phone:

a) Dial with the handset resting in the cradle, or

b) Pick up the handset or press handsfree and then dial the number.

The phone shows the current communication status in the display.

Terminate a call:

To end calls:

a) Place the handset on its cradle, or

b) Press the hook switch, or

c) Press GOODBYE.

The phone will terminate the call and return to the idle state.

Accept a call:

Pick up the handset or press HANDSFREE to accept incoming calls. The phone is now in a call.

Send an incoming call to Voicemail:

Press IGNORE the while the phone is ringing to send the call to your voicemail.

Transfer

Direct Transfer while on a call:

a) Press the TRANSFER key to put the connected party.

b) Dial the number to which the call is to be directly transferred.

c) You have the option to wait until the other party answers.

d) Press TRANSFER again to complete the transfer.

Transfer Call to Voicemail:

a) Press the TRANSFER key.

b) Dial * followed by the extension number.

c) Immediately press TRANSFER.

Conference

For your extension and two other calls:

a) Make the first call.

b) Press CONFERENCE.

c) Make the second call.

d) Press CONFERENCE again.  All three parties will be joined.

Ring Tone, Brightness

Change ring tone or brightness level:

a) Press OPTIONS.

b) Press “Audio” then select “Tone 1” through “Tone 5”, or

c) Press “Display” and choose “Level 1” through “Level 5”.

Adjust Volume:

In the idle state or while making a call, you can use the keys to increase or lower the volume. The audio device (speaker/handset/headset) that you are currently using will be adjusted.

Mute / Unmute:

To mute the microphone during a call, press the MUTE key. Press the MUTE key again to enable the microphone.

Handset / Handsfree / Headset:

The phone supports calls made using the handset, a headset, or the handsfree capability. During a call, it is possible to switch between modes by pressing the green HANDSFREE key.

When a headset is connected and the audio output is set to headset, the phone will treat the headset as the output device for calls, which is indicated during a call by a flashing light next to HANDSFREE. When the phone is used in a call center environment, the connected headset will usually be the default setting for speaking on the phone. The key is therefore used to accept incoming calls.

Bluetooth

Add and select a Bluetooth headset:

a) Press OPTIONS.

b) Press “Audio” then select “Headset Device: Bluetooth”.

c) Press the back arrow.

d) Press BLUETOOTH and turn it on by pressing the red stop sign until it

becomes a green checkmark.

e) Press the plus sign beside “Add new device”.

f) Press SEARCH and put your headset into discovery mode.

g) Select your headset and enter the headset’s PIN (usually 0000).

h) You will see the headset in a list; it can be removed with the red “X”.

i) Press the GOODBYE key.

j) You should now be able to answer, originate, and hang-up calls with

the button on your headset.

OPTIONAL FUNCTIONS

This section describes the use of optional customized features for the Aastra telephones.  These features will be shown on the softkeys beside the display.  There is usually a MORE key in the lower right which displays additional features beyond the initial screen.  You may not have all of the functions listed in this manual available on your system.

Call Forward:

To enable Call Forwarding:

a) Press CALL FWD.

b) Press ACTIVATE.

c) Select “Enter Number” and input the destination phone number, or

d) Select one of your pre-entered Personal Numbers.

e) Press SUBMIT.

To disable Call Forwarding follow the same steps but press DEACTIVATE instead of ACTIVATE.

You can edit your pre-programmed Personal Numbers by pressing CALL FWD then MY NUMBERS.

Call List:

The phone maintains lists of missed, received, and dialled calls.  To access the list of incoming calls press CALLER’S LIST KEY.  Press the down arrow to begin scrolling through the numbers from the most recent to the oldest.  The display will show either a check mark or an exclamation mark to indicate whether the call was answered or not.

For outgoing calls press REDIAL and use the arrow keys to scroll through the list.

Press DIAL to call the highlighted number.

Directory:

The phone contains a list of extensions that can be accessed from the phone’s idle state by pressing the DIRECTORY key.

DND Mode on/off:

DND is short for “Do Not Disturb”. If this mode is activated with the DND button incoming calls will no longer come through to the phone and you will be completely undisturbed by the phone. If there is a mailbox set up for you, the call will go there. In idle mode, “DND activated” is displayed on the screen when DND is activated.  Press it again to de-activate.

Follow-Me:

Follow me is a feature that causes incoming calls ring multiple phones simultaneously.  For example, calls to your extension could be set to ring on your cell phone and a co-workers extension at the same time they ring your desk phone.  This feature must be turned on by a system administrator before you can use it.

Enable Follow-Me:

a) Press FOLLOW-ME.

b) Press the arrow beside STATUS until you see “Status: Activated”.

c) Press down arrow until you see “x phone numbers”.

d) Press the blue arrow beside “x phone numbers”.

e) Press ADD INTERNAL and select an extension from the list, or

f) Press ADD EXTERNAL and enter the 10 digit phone number.

Disable Follow-Me:

a) Press FOLLOW-ME.

b) Press the arrow beside STATUS until you see “Status: Deactivated”.

Keys:

Add, Remove, or Change Softkeys:

a) Press KEYS.

b) Use DOWN ARROW or NEXT PAGE to view the list of keys.

c) Press the BLUE ARROW, REMOVE, MOVE UP, or MOVE DOWN.

When adding a new key you have the option to select type “Busy Lamp Field” (displays the status of an extension) or “Speed Dial”.

Logout

Press the LOGOUT key, enter your voicemail password, select LOGOUT, then press SUBMIT to remove your extension number from the phone and prepare it for a new extension number.  To log back in enter your extension number and voicemail password then press SUBMIT.  The logout/login sequence will update the display name on the telephone if it has been changed in system programming.

Meet Me Conference (Conference Bridge)

For multiple party conferences:

A conference bridge may have been configured in your phone system, usually at extension 300.  The conference PIN will also be pre-configured – usually it is set to 5276.

From inside the office:

a) Dial the conference bridge extension number

b) Enter your PIN at the voice prompt.

From outside the office:

a) Call in and get transferred to the conference bridge ext. number

b) Enter your PIN at the voice prompt.

The only limit to the number of attendees is the physical limit of outside trunks.

Park and Retrieve Calls

Park:
To “Park” a call is to put it on hold in a place that anyone else can retrieve it. While in a call press the button labelled PARK.

Retrieve:
To Retrieve a parked call pick up the handset then dial the number the call is parked on (101, 102, …).  To view a list of currently parked calls press PARKING while your phone is on-hook.

Presence:

Press the PRESENCE button to let co-workers know you are out of the office when they use they call your extension. Pick your new status by pressing CHG STATUS.  Your display will show your current status. Pick I AM BACK to turn it off.

After changing your status you have the option to press TEMP MSG which allows you to record a temporary greeting in your voicemail that is deleted when your status changes to “I am Back”.  You can also press RETURN to input the date and time you will be returning.

Press WHERE IS? to view the extension list and statuses.

Press PREFERENCES to change the default action for a given status.  For example, anytime your status is set to “In a Meeting” your phone can automatically go into DND mode.

Voicemail

Message Waiting Indication (MWI):

If there are messages in your mailbox the idle screen shows that a recorded message is waiting for you and the Message Light will be flashing.

Connect to your mailbox with the MESSAGES key. You will be asked for your password; the default is 9876.  NOTE: If you are on speakerphone when you select a message you will remain on speakerphone as long as you are listening to that message.  An alternate method for accessing voicemail is to dial *97.

Change your password:

a) Press the MESSAGES key and enter your password.

b) Press OPTIONS.

c) Ensure the arrow is at “Change Password” and press SELECT.

d) Enter your new password and press SUBMIT.

Record your name:

a) Press the MESSAGES key and enter your password.

b) Press OPTIONS.

c) Point to “Record Name” or “Modify Name” and press SELECT.

d) The system will tell you to say your name.

e) Record only your name and press # to end recording.

Recording unavailable, busy or temporary greetings:

a) Press the MESSAGES key and enter your password.

b) Press OPTIONS.

c) Point to “Record” or “Modify” for the greeting you want.

d) Press SELECT.

e) The system will tell you to begin recording.

f) Say the greeting and press # to end recording.

Access Voicemail from outside the office:

a) Call your direct line and wait for your voicemail message to start.

b) When it answers, press the * key then enter your password.

c) Follow the voice prompts to listen to messages, etc.